## Slide 1: Camera calibration

## Slide 2: References
http://szeliski.org/Book/
http://www.cs.cornell.edu/courses/cs5670/2019sp/lectures/lectures.html
http://www.cs.cmu.edu/~16385/

## Slide 3
Camera intrinsics
Camera extinsics
Radial distortion

## Slide 4: What is camera calibration
Geometric camera calibration, also referred to as camera resectioning, estimates the parameters of a lens, image sensor, position and view direction of a perspective camera.
You can use these parameters to correct for lens distortion, measure the size of an object in world units, or determine the location of the camera in the scene. These tasks are used in applications such as machine vision to detect and measure objects. They are also used in robotics, for navigation systems, and 3-D scene reconstruction.
[from: https://www.mathworks.com/help/vision/ug/camera-calibration.html]

## Slide 5: Starting from the end
The camera matrix is a full transformation from 3D objects in the scene to a 2D image with the specific camera parameters:
How many DOFs do we have?
Notes: \\
P =
\begin{bmatrix}a_{11} & a_{12}&a_{13}&a_{14}
\\ a_{21}&a_{22} &a_{23}&a_{24}
\\a_{31}&a_{32}&a_{33}&a_{34}
\end{bmatrix}
\\
P
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}u
\\ v
\\w
\end{bmatrix}
\mapsto
\begin{bmatrix}\frac{u}{w}
\\ \frac{v}{w}
\end{bmatrix}

## Slide 6: Starting from the end
The camera matrix is a full transformation from 3D objects in the scene to a 2D image with the specific camera parameters:
How many DOFs do we have?
  11, because in homogenous coordinates the answer is always correct up to a scale.
Notes: \\
P =
\begin{bmatrix}a_{11} & a_{12}&a_{13}&a_{14}
\\ a_{21}&a_{22} &a_{23}&a_{24}
\\a_{31}&a_{32}&a_{33}&a_{34}
\end{bmatrix}
\\
P
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}u
\\ v
\\w
\end{bmatrix}
\mapsto
\begin{bmatrix}\frac{u}{w}
\\ \frac{v}{w}
\end{bmatrix}

## Slide 7: Starting from the end
Intrinsic camera matrix:
estimates the parameters of the lens and image sensor.
Perspective projection matrix:
Project from 3D to 2D as seen before:
extrinsic camera matrix:
estimates the parameters of position and view direction of a camera.
Notes: P_{3X4} = K_{3X3}[I|0]_{3X4}\Pi_{4X4}

## Slide 8
intrinsic

## Slide 9: Coordinate systems
There are 3 coordinate systems that are discussed in general:
world point
image point

## Slide 10: Recap: perspective projection
Perspective projection (also known as perspective transformation) is a linear projection where three dimensional objects are projected on the image plane.
image plane
principal axis
Notes: \begin{bmatrix}x
\\ y
\\ z
\end{bmatrix}
\begin{bmatrix}u
\\ v
\end{bmatrix}

## Slide 11: Recap: perspective projection
image plane
Using triangle proportions (Thales’ theorem) we can easily conclude that:
Notes: \begin{bmatrix}x
\\ y
\\ z
\end{bmatrix}
\mapsto
\begin{bmatrix}u
\\ v
\end{bmatrix}
=
\begin{bmatrix}f\frac{x}{z}
\\ f\frac{y}{z}
\end{bmatrix}

## Slide 12: Recap: perspective projection
Let’s use the homogeneous coordinates:
  Units of
Notes: \begin{bmatrix}f & 0&0&0
\\ 0&f &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}fx
\\ fy
\\z
\end{bmatrix}
\mapsto
\begin{bmatrix}f\frac{x}{z}
\\ f\frac{y}{z}
\end{bmatrix}

## Slide 13: Recap: perspective projection
Let’s split into 2 matrices and use 3D->2D homogenous coordinates:
Intrinsic camera matrix
Perspective projection matrix
Notes: \begin{bmatrix}f & 0&0
\\ 0&f &0
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & 0&0&0
\\ 0&1 &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}fx
\\ fy
\\z
\end{bmatrix}
\mapsto
\begin{bmatrix}f\frac{x}{z}
\\ f\frac{y}{z}
\end{bmatrix}

## Slide 14: Intrinsic camera matrix
The intrinsic matrix contains 5 intrinsic parameters. These parameters encompass:
  Scaled x & y focal length.
  Sensor skew.
  Principal point.
The intrinsic camera matrix transforms a point in general image plane 2D space to the camera specific image space.
Notes: K =
\begin{bmatrix}f & 0&0
\\ 0&f &0
\\0&0&1
\end{bmatrix}

## Slide 15: Intrinsic camera matrix
Transforming to units of pixels in image space:
  Pixel size in x dimension is and Pixel size in y dimension is
Notes: K =
\begin{bmatrix}f_x & 0&0
\\ 0&f_y &0
\\0&0&1
\end{bmatrix}

## Slide 16: Intrinsic camera matrix
Let’s add the principle point: the offset vector between the camera coordinates to the image coordinate [units of pixels].
How to add this to the intrinsic matrix?
camera coordinate system
image coordinate system
image plane

## Slide 17: Intrinsic camera matrix
Let’s add the principle point: the offset vector between the projected camera coordinates to the image coordinate [units of pixels].
How to add this to the intrinsic matrix?
image plane

## Slide 18: Intrinsic camera matrix
In some camera sensors exist a very small skew which makes the sensor a parallelogram.
Notes: K =
\begin{bmatrix}f_x & s&p_x
\\ 0&f_y &p_y
\\0&0&1
\end{bmatrix}
==============================
Kx =
\begin{bmatrix}1 & 0&p_x
\\ 0&1 &p_y
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & \frac{s}{f_y}&0
\\ 0&1 &0
\\0&0&1
\end{bmatrix}
\begin{bmatrix}f_x & 0&0
\\ 0&f_y &0
\\0&0&1
\end{bmatrix}
x

## Slide 19: Extrinsic camera matrix
The extrinsic camera matrix is a concatenation of a rotation and translation matrix from to
We need the world coordinate system when we are talking about multiple camera setup and the relations between one another.
We are given a point in world coordinates and we transform it to the camera coordinate system

## Slide 20: Extrinsic camera matrix
We are given a point in world coordinates and we transform it to the camera coordinate system:

## Slide 21: Extrinsic camera matrix
World coordinate system
Camera coordinate system

## Slide 22: Extrinsic camera matrix
World coordinate system
Camera coordinate system
Translation vector from world to camera

## Slide 23: Extrinsic camera matrix

## Slide 24: Extrinsic camera matrix
Rotation matrix from world to camera

## Slide 25: Extrinsic camera matrix
Transform to homogenous coordinate notation:
Translation part: 3 DOFs.
Rotation part: 3 DOFs (, , ).

## Slide 26: Full camera matrix
Notes: P =
\begin{bmatrix}f_x & s&p_x
\\ 0&f_y &p_y
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & 0&0&0
\\ 0&1 &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}R_{3X3} & -RC_{3X1}
\\ 0_{1X3}&1
\end{bmatrix}
=========================================
\begin{bmatrix}u
\\ v
\\w
\end{bmatrix}
=
\begin{bmatrix}f_x & s&p_x
\\ 0&f_y &p_y
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & 0&0&0
\\ 0&1 &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}R_{3X3} & -RC_{3X1}
\\ 0_{1X3}&1
\end{bmatrix}
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}

## Slide 27
Camera calibration
Assuming we are given an imaged points and their corresponding 3D points in the real world, camera calibration is the process to find the camera parameters.
  We will return to this assumption later.

## Slide 28
Heterogeneous coordinates
(non-linear relation between coordinates)
Camera calibration

## Slide 29
Make them linear with algebraic manipulation…
Now we can setup a system of linear equations with multiple point correspondences
Camera calibration

## Slide 30
In matrix form …
Vector of 1X12
Camera calibration

## Slide 31
In matrix form …
For N points …
How do we solve this system?
Camera calibration
How many points do we need to solve this problem?

## Slide 32
Camera calibration
We’ve already seen this minimization problem in the curve fitting class- linear TLS.
6 points will give us 12 equations- enough for 11 parameters.

## Slide 33: Linear TLS -the minimization problem
The minimization problem is:
Recall eigendecomposition:
  Also recall that each eigenvector is normalized
  ().
The solution to the minimization problem above is the eigenvector corresponding to smallest eigenvalue of .
Watch out: trying to minimize the problem above without the constraint will result with the trivial solution of
Notes: Av = \lambda v \mapsto v^TAv = \lambda

## Slide 34
Camera calibration
The second part is to decompose the resulted matrix into and.
We can look at the resulted matrix as follows:
Finding : take only the rightmost column of and multiply it from the left by .
Finding K & R: RQ decomposition of to upper triangular matrix and orthogonal matrix.
  The exact definition is out of scope. Read more about it here: http://ksimek.github.io/2012/08/14/decompose/

## Slide 35
AR using markers
Compute point correspondents of known marker.
Estimate the pose of the camera.
Project 3D content to image plane using known places of camera and marker.
Examples:
  https://www.youtube.com/watch?v=lIHcnwOVKng
  https://developers.google.com/ar/develop/c/augmented-images

## Slide 36: Correcting radial distortion
Radial distortion of the image
  Caused by imperfect lenses
  Deviations are most noticeable for rays that pass through the edge of the lens
No distortion
Pin cushion
Barrel

## Slide 37: Correcting radial distortion

## Slide 38
Correcting radial distortion
…) …)
Where:
  : distorted image points. Given.
  : distortion center (principle point). Known from calibration (may need iterative calibration to find this and ).
  : undistorted image points. Known from calibration plane.
  . Known from above.
  coefficients. unknowns

## Slide 39: Correcting radial distortion
How do we solve this? We’ve seen something similar in HW5- simple LS should do the trick.

## Slide 40
Camera calibration- the assumption
Assuming we are given an imaged points and their corresponding 3D points in the real world, camera calibration is the process to find the camera parameters.
We can get 3D points of the world by calibrating with a known size calibration object- like a checkerboard plane.
https://www.microsoft.com/en-us/research/wp-content/uploads/2016/02/tr98-71.pdf

## Slide 41
http://www.vision.caltech.edu/bouguetj/calib_doc/htmls/example.html
https://docs.opencv.org/2.4/doc/tutorials/calib3d/camera_calibration/camera_calibration.html
https://webcourse.cs.technion.ac.il/236873/Winter2017-2018/ho/WCFiles/Camera%20Calibration.pdf
http://ksimek.github.io/2012/08/13/introduction/