## Slide 1: Camera calibration

## Slide 2: References
http://szeliski.org/Book/
http://www.cs.cornell.edu/courses/cs5670/2019sp/lectures/lectures.html
http://www.cs.cmu.edu/~16385/

## Slide 3: Contents
What is camera calibration?
Camera intrinsics
Camera extrinsics
Full camera matrix
Calibration methods and distortions

## Slide 4: What is camera calibration
Geometric camera calibration, also referred to as camera resectioning, estimates the parameters of a lens, image sensor, position and view direction of a perspective camera.
You can use these parameters to correct for lens distortion, measure the size of an object in world units, or determine the location of the camera in the scene. These tasks are used in applications such as machine vision to detect and measure objects. They are also used in robotics, for navigation systems, and 3-D scene reconstruction.
[from: https://www.mathworks.com/help/vision/ug/camera-calibration.html]

## Slide 5: Starting from the end
The camera matrix is a full transformation from 3D objects in the scene to a 2D image with the specific camera parameters:
How many DOFs do we have?
Notes: \\
P =
\begin{bmatrix}a_{11} & a_{12}&a_{13}&a_{14}
\\ a_{21}&a_{22} &a_{23}&a_{24}
\\a_{31}&a_{32}&a_{33}&a_{34}
\end{bmatrix}
\\
P
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}u
\\ v
\\w
\end{bmatrix}
\mapsto
\begin{bmatrix}\frac{u}{w}
\\ \frac{v}{w}
\end{bmatrix}

## Slide 6: Starting from the end
The camera matrix is a full transformation from 3D objects in the scene to a 2D image with the specific camera parameters:
How many DOFs do we have?
  11, because in homogenous coordinates the answer is always correct up to a scale.
Notes: \\
P =
\begin{bmatrix}a_{11} & a_{12}&a_{13}&a_{14}
\\ a_{21}&a_{22} &a_{23}&a_{24}
\\a_{31}&a_{32}&a_{33}&a_{34}
\end{bmatrix}
\\
P
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}u
\\ v
\\w
\end{bmatrix}
\mapsto
\begin{bmatrix}\frac{u}{w}
\\ \frac{v}{w}
\end{bmatrix}

## Slide 7: Starting from the end
Intrinsic camera matrix:
estimates the parameters of the lens and image sensor.
Perspective projection matrix:
Project from 3D to 2D as seen before:
extrinsic camera matrix:
estimates the parameters of position and view direction of a camera.
Notes: P_{3X4} = K_{3X3}[I|0]_{3X4}\Pi_{4X4}

## Slide 8: Contents
What is camera calibration?
Camera intrinsics
Camera extrinsics
Full camera matrix
Calibration methods and distortions

## Slide 9: Coordinate systems
There are 3 coordinate systems that are discussed in general: camera, world and image coordinate systems.
world point
image point

## Slide 10: Recap: perspective projection
Perspective projection (also known as perspective transformation) is a linear projection where three dimensional objects are projected on the image plane.
image plane
principal axis
Notes: \begin{bmatrix}x
\\ y
\\ z
\end{bmatrix}
\begin{bmatrix}u
\\ v
\end{bmatrix}

## Slide 11: Recap: perspective projection
image plane
Using triangle proportions (Thales’ theorem) we can easily conclude that:
Notes: \begin{bmatrix}x
\\ y
\\ z
\end{bmatrix}
\mapsto
\begin{bmatrix}u
\\ v
\end{bmatrix}
=
\begin{bmatrix}f\frac{x}{z}
\\ f\frac{y}{z}
\end{bmatrix}

## Slide 12: Recap: perspective projection
Let’s use the homogeneous coordinates:
  Units of
Notes: \begin{bmatrix}f & 0&0&0
\\ 0&f &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}fx
\\ fy
\\z
\end{bmatrix}
\mapsto
\begin{bmatrix}f\frac{x}{z}
\\ f\frac{y}{z}
\end{bmatrix}

## Slide 13: Recap: perspective projection
Let’s split into 2 matrices and use 3D->2D homogenous coordinates:
Intrinsic camera matrix
Perspective projection matrix
Notes: \begin{bmatrix}f & 0&0
\\ 0&f &0
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & 0&0&0
\\ 0&1 &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\begin{bmatrix}fx
\\ fy
\\z
\end{bmatrix}
\mapsto
\begin{bmatrix}f\frac{x}{z}
\\ f\frac{y}{z}
\end{bmatrix}

## Slide 14: Intrinsic camera matrix
The intrinsic matrix contains 5 intrinsic parameters. These parameters encompass:
  Scaled x & y focal length.
  Sensor skew.
  Principal point.
The intrinsic camera matrix transforms a point in general image plane 2D space to the camera specific image space.
Notes: K =
\begin{bmatrix}f & 0&0
\\ 0&f &0
\\0&0&1
\end{bmatrix}

## Slide 15: Intrinsic camera matrix
Transforming to units of pixels in image space:
  Pixel size in x dimension is and Pixel size in y dimension is
Notes: K =
\begin{bmatrix}f_x & 0&0
\\ 0&f_y &0
\\0&0&1
\end{bmatrix}

## Slide 16: Intrinsic camera matrix
Let’s add the principle point: the offset vector between the projected camera coordinates to the image coordinate [units of pixels].
How to add this to the intrinsic matrix?
image plane

## Slide 17: Intrinsic camera matrix
Let’s add the principle point: the offset vector between the projected camera coordinates to the image coordinate [units of pixels].
How to add this to the intrinsic matrix?
image plane

## Slide 18: Intrinsic camera matrix
In some camera sensors exist a very small skew which makes the sensor a parallelogram.
Notes: K =
\begin{bmatrix}f_x & s&p_x
\\ 0&f_y &p_y
\\0&0&1
\end{bmatrix}
==============================
Kx =
\begin{bmatrix}1 & 0&p_x
\\ 0&1 &p_y
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & \frac{s}{f_y}&0
\\ 0&1 &0
\\0&0&1
\end{bmatrix}
\begin{bmatrix}f_x & 0&0
\\ 0&f_y &0
\\0&0&1
\end{bmatrix}
x

## Slide 19: Contents
What is camera calibration?
Camera intrinsics
Camera extrinsics
Full camera matrix
Calibration methods and distortions

## Slide 20: Extrinsic camera matrix
The extrinsic camera matrix is a concatenation of a rotation and translation matrix from to
We need the world coordinate system when we are talking about multiple camera setup and the relations between one another.
We are given a point in world coordinates and we transform it to the camera coordinate system

## Slide 21: Extrinsic camera matrix
We are given a point in world coordinates and we transform it to the camera coordinate system:

## Slide 22: Extrinsic camera matrix
World coordinate system
Camera coordinate system

## Slide 23: Extrinsic camera matrix
World coordinate system
Camera coordinate system
Translation vector from world to camera

## Slide 24: Extrinsic camera matrix

## Slide 25: Extrinsic camera matrix
Rotation matrix from world to camera

## Slide 26: Extrinsic camera matrix
Transform to homogenous coordinate notation:
Translation part: 3 DOFs.
Rotation part: 3 DOFs (, , ).
In OpenCV they do a different transformation that first does a rotation and then translation:

## Slide 27: Contents
What is camera calibration?
Camera intrinsics
Camera extrinsics
Full camera matrix
Calibration methods and distortions

## Slide 28: Full camera matrix
Notes: P =
\begin{bmatrix}f_x & s&p_x
\\ 0&f_y &p_y
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & 0&0&0
\\ 0&1 &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}R_{3X3} & -RC_{3X1}
\\ 0_{1X3}&1
\end{bmatrix}
=========================================
\begin{bmatrix}u
\\ v
\\w
\end{bmatrix}
=
\begin{bmatrix}f_x & s&p_x
\\ 0&f_y &p_y
\\0&0&1
\end{bmatrix}
\begin{bmatrix}1 & 0&0&0
\\ 0&1 &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}R_{3X3} & -RC_{3X1}
\\ 0_{1X3}&1
\end{bmatrix}
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}

## Slide 29: Side note: normalized image coordinates
A projection into 2D where the intrinsic matrix is already embedded at the coordinate given
We will use it when we already know the intrinsic of the camera and just interested in the extrinsic:
Notes: \\
\begin{bmatrix}\widetilde{u}
\\ \widetilde{v}
\\\widetilde{w}
\end{bmatrix}
=
K^{-1}
\begin{bmatrix}u
\\ v
\\w
\end{bmatrix}
=
\begin{bmatrix}1 & 0&0&0
\\ 0&1 &0&0
\\0&0&1&0
\end{bmatrix}
\begin{bmatrix}R_{3X3} & -RC_{3X1}
\\ 0_{1X3}&1
\end{bmatrix}
\begin{bmatrix}x
\\ y
\\z
\\1
\end{bmatrix}
=
\\
R
\begin{bmatrix}x
\\ y
\\z
\end{bmatrix}
-RC
=
R
\begin{bmatrix}x
\\ y
\\z
\end{bmatrix}
+t

## Slide 30
Full camera matrix
Assuming we are given an imaged points and their corresponding 3D points in the real world, camera calibration is the process to find the camera parameters.
  We will return to this assumption later.

## Slide 31
Heterogeneous coordinates
(non-linear relation between coordinates)
Full camera matrix

## Slide 32
Make them linear with algebraic manipulation…
Now we can setup a system of linear equations with multiple point correspondences
Full camera matrix

## Slide 33
In matrix form …
Vector of 1X12
Full camera matrix

## Slide 34
For N points …
How do we solve this system?
Full camera matrix
How many points do we need to solve this problem?
In matrix form …

## Slide 35
Full camera matrix
We’ve already seen this minimization problem in the curve fitting class- linear TLS.
6 points will give us 12 equations- enough for 11 parameters.

## Slide 36: Linear TLS -the minimization problem
The minimization problem is:
Recall eigendecomposition:
  Also recall that each eigenvector is normalized
  ().
The solution to the minimization problem above is the eigenvector corresponding to smallest eigenvalue of .
Watch out: trying to minimize the problem above without the constraint will result with the trivial solution of
Notes: Av = \lambda v \mapsto v^TAv = \lambda

## Slide 37
Full camera matrix
The second part is to decompose the resulted matrix into and.
We can look at the resulted matrix as follows:
Finding : take only the rightmost column of and multiply it from the left by .
Finding K & R: RQ decomposition of to upper triangular matrix and orthogonal matrix.
  The exact definition is out of scope. Read more about it here: http://ksimek.github.io/2012/08/14/decompose/

## Slide 38: Contents
What is camera calibration?
Camera intrinsics
Camera extrinsics
Full camera matrix
Calibration methods and distortions

## Slide 39: Geometric calibration
Place a known object in the scene:
  identify correspondences between image and scene
  compute mapping from scene to image
Issues:
  must know geometry very accurately
  must know 3D->2D correspondence

## Slide 40: Geometric calibration
Advantages:
  Very simple to formulate.
  Analytical solution.
Disadvantages:
  Doesn’t model radial/ tangential distortion.
For these reasons, nonlinear methods are preferred.
  Define error function E between projected 3D points and image points.
  E encompass intrinsics, extrinsics, radial distortion and tangential distortion.
  Minimize E using nonlinear optimization techniques.

## Slide 41
AR using markers
Compute point correspondents of known marker.
Estimate the pose of the camera.
Project 3D content to image plane using known places of camera and marker.
Examples:
  https://www.youtube.com/watch?v=lIHcnwOVKng
  https://developers.google.com/ar/develop/c/augmented-images

## Slide 42: Radial distortion
Radial distortion of the image
  Caused by imperfect lenses
  Deviations are most noticeable for rays that pass through the edge of the lens
No distortion
Pin cushion
Barrel

## Slide 43: Radial distortion

## Slide 44: Radial distortion
before
after

## Slide 45
Radial distortion
…) …)
Where:
  : distorted image points. Given.
  : distortion center (principle point). Known from calibration (may need iterative calibration to find this and ).
  : undistorted image points. Known from calibration plane.
  . Known from above.
  coefficients. unknowns

## Slide 46: Tangential distortion
Another kind of distortion caused by the camera sensor not being completely parallel to the lens and image plane.

## Slide 47: Tangential distortion

## Slide 48
Multi plane calibration
Advantages:
  Only requires a plane
  Don’t have to know positions/orientations
Disadvantage:
  Need to solve non-linear optimization problem.
https://www.microsoft.com/en-us/research/wp-content/uploads/2016/02/tr98-71.pdf