## Slide 1: Features

## Slide 2: References
http://szeliski.org/Book/
http://www.cs.cornell.edu/courses/cs5670/2019sp/lectures/lectures.html
http://www.cs.cmu.edu/~16385/
https://medium.com/software-incubator/introduction-to-orb-oriented-fast-and-rotated-brief-4220e8ec40cf
https://opencv-python-tutroals.readthedocs.io/en/latest/py_tutorials/py_feature2d/py_table_of_contents_feature2d/py_table_of_contents_feature2d.html
https://towardsdatascience.com/sift-scale-invariant-feature-transform-c7233dc60f37

## Slide 3
Feature detection
  Talk about harris corner detector?
Feature descriptor and matching
Sift
  Talk about orb
Panorama

## Slide 4: What is a feature?
There is no universal or exact definition of what constitutes a feature, and the exact definition often depends on the problem or the type of application. Given that, a feature is defined as an "interesting" part of an image.
  [from: wikipedia]

## Slide 5: What can we do with features?
Object recognition
Robot navigation
Panorama stitching

## Slide 6: Local features: main components
1. Detection: Identify the interest points (also called keypoints).
2. Description: Extract vector feature descriptor surrounding each interest point.
3. Matching: Determine correspondence between descriptors in two views.

## Slide 7: detection

## Slide 8: Global detection
Template matching

## Slide 9: Advantages of local keypoints
Locality:
  features are local, so robust to occlusion and clutter
Quantity:
  hundreds or thousands in a single image
Distinctiveness:
  can differentiate a large database of objects
Efficiency
  real-time performance achievable

## Slide 10: Local measures of uniqueness
Suppose we only consider a small window of pixels.
How does the window change when you shift it?
Credit: S. Seitz, D. Frolova, D. Simakov
Notes: High level idea is that corners are good. You want to find windows that contain strong gradients AND gradients oriented in more than one direction

## Slide 11: Local measures of uniqueness
“flat” region: no change in all directions
“edge”:
no change along the edge direction
“corner”: significant change in all directions
Suppose we only consider a small window of pixels-
How does the window change when you shift it?

## Slide 12: Harris corner detection: probabilistic interpretation
1. Compute image gradients over a small region
array of x gradients
array of y gradients

## Slide 13: Harris corner detection: probabilistic interpretation
What does the distribution tell you about the region?
1. Compute image gradients over a small region

## Slide 14: Harris corner detection: probabilistic interpretation
distribution reveals edge orientation and magnitude
1. Compute image gradients over a small region

## Slide 15: Harris corner detection: probabilistic interpretation
2. Subtract the mean from each image gradient
plot intensities
constant intensity gradient
intensities along the line
plot of image gradients
subtract mean

## Slide 16: Harris corner detection: probabilistic interpretation
plot intensities
constant intensity gradient
intensities along the line
plot of image gradients
data is centered
(‘DC’ offset is removed)
subtract mean
2. Subtract the mean from each image gradient

## Slide 17: Harris corner detection: probabilistic interpretation
3. Compute the covariance matrix
As you know:
  Covariance of two random variables:
  Covariance matrix (also known as second moment matrix) of two random vectors:
In our case and due to step 2.
Notes: \begin{align}
\operatorname{Cov}(X,Y) &= \operatorname{E}\left[(X - \operatorname{E}[X])(Y - \operatorname{E}[Y])\right] \nonumber\\
&= \operatorname{E}\left[XY -X\operatorname{E}[Y] -Y\operatorname{E}[X] + \operatorname{E}[X]\operatorname{E}[Y]\right] \nonumber\\
&= \operatorname{E}\left[XY\right] - 2\operatorname{E}[X]\operatorname{E}[Y] + \operatorname{E}[X]\operatorname{E}[Y] \nonumber\\
&= \operatorname{E}\left[XY\right] -\operatorname{E}[X]\operatorname{E}[Y] \nonumber
\end{align}
=================================
\operatorname{K}_{\mathbf{X}\mathbf{X}} = \operatorname{cov}[\mathbf{X},\mathbf{Y}] = \operatorname{E}[(\mathbf{X}-\mathbf{\mu_X})(\mathbf{Y}-\mathbf{\mu_Y})^{\rm T}]= \operatorname{E}[\mathbf{X} \mathbf{Y}^T] - \mathbf{\mu_X}\mathbf{\mu_Y}^T

## Slide 18: Harris corner detection: probabilistic interpretation
3. Compute the covariance matrix
array of x gradients
array of y gradients
.*
=sum(
)

## Slide 19: Harris corner detection
Consider shifting the window W by (u,v)
  compare each pixel before and after by summing up the squared differences (SSD).
  this defines an SSD “error” :
We are happy if this error is high for all
W
(u,v)

## Slide 20: Harris corner detection
Taylor Series expansion of :
If the motion is small, then first order approximation is good
Plug it into the SSD error term:

## Slide 21: Harris corner detection
u
v
E(u,v)
Also called second-moments matrix

## Slide 22: Harris corner detection
Horizontal edge:
u
v
E(u,v)

## Slide 23: Harris corner detection
Vertical edge:
u
v
E(u,v)

## Slide 24
A real symmetric matrix has an eigendecomposition of:
  Bonus: eigenvectors are orthonormal if A is real and symmetric.
4. Compute the eigendecomposition
Harris corner detection: probabilistic interpretation
Notes: \\
Av = \lambda v
\\
AQ=Q\Lambda
\\
A=Q\Lambda Q^{-1}
\\
\xrightarrow{\text{A is real symmetric matrix}}
\\
A=Q\Lambda Q^{T}
\\
A=\left(\begin{array}{ll}{e_{1}} & {e_{2}}\end{array}\right)\left(\begin{array}{cc}{\lambda_{1}} & {0} \\ {0} & {\lambda_{2}}\end{array}\right)\left(\begin{array}{c}{e_{1}^{T}} \\ {e_{2}^{T}}\end{array}\right)

## Slide 25: Harris corner detection
An ellipse can have a matrix form of:
Which is exactly as a rotated ellipse with a center of
Notes: \\
x^{T}\left(e_{1} e_{2}\right)\left(\begin{array}{cc}{\lambda_{1}} \\ {} & {\lambda_{2}}\end{array}\right)\left(\begin{array}{c}{e_{1}^{T}} \\ {e_{2}^{T}}\end{array}\right) x=1
\\
\lambda_{1} x^{T} e_{1} e_{1}^{T} x+\lambda_{2} x^{T} e_{2} e_{2}^{T} x =1
\\
\frac{\left(e_{1}^{T} x\right)^{2}}{\left(\frac{1}{\sqrt{\lambda_{1}}}\right)^{2}}+\frac{\left(e_{2}^{T} x\right)^{2}}{\left(\frac{1}{\sqrt{\lambda_{2}}}\right)^{2}}=1
=============================================
\frac{(x \cos (\theta)+y \sin (\theta))^{2}}{a^2}+\frac{(x \sin (\theta)-y \cos (\theta))^2}{b^{2}}=1

## Slide 26: Harris corner detection
Combining the two equations seen before we can conclude that when taking a cross-section from the error function, we can get an ellipsoid.
Assume
Remember to subtract the mean of each patch so that the ellipsoid is centered.
direction of
direction of
(max)-1/2
(min)-1/2

## Slide 27: Harris corner detection
Eigenvalues and eigenvectors of
  = direction of largest increase in
  = relative increase in direction
  = direction of smallest increase in
  = relative increase in direction
direction of
direction of
(max)-1/2
(min)-1/2

## Slide 28: Interpreting the eigenvalues
A “good” corner will have a large , which means big change of in both axis.
Getting the eigenvectors and eigenvalues is computationally inefficient.
Instead, use two tricks:
Then we can more easily compute

## Slide 29: Interpreting the eigenvalues
1
2
“Corner” 1 and 2 are large, 1 ~ 2; E increases in all directions
1 and 2 are small; E is almost constant in all directions
“Edge” 1 >> 2
“Edge” 2 >> 1
“Flat” region

## Slide 30: Interpreting the eigenvalues
A binary threshold of pixels above and

## Slide 31: Harris corner detection
Compute gradients of patch around each pixel.
Subtract the mean from each patch gradient.
Compute the covariance matrix.
Compute eigendecomposition of covariance matrix.
Use eigenvalues to find corners.
This is PCA (principal component analysis). Out of scope but really interesting!

## Slide 32: Harris detector example

## Slide 33: f value (red high, blue low)

## Slide 34: Threshold (f > value)

## Slide 35: Find local maxima of f

## Slide 36: Harris features (in red)

## Slide 37: Weighting the derivatives
In practice, using a simple window W doesn’t work too well
Instead, we’ll weight each derivative value based on its distance from the center pixel

## Slide 38
Gaussian
Laplacian

## Slide 39: Invariant local features
Find features that are invariant to transformations
  geometric invariance: translation, rotation, scale
  photometric invariance: brightness, exposure, …
Feature Descriptors

## Slide 40: Why extract features?
Motivation: panorama stitching
  We have two images – how do we combine them?

## Slide 41: Why extract features?
Motivation: panorama stitching
  We have two images – how do we combine them?
Step 1: extract features
Step 2: match features

## Slide 42: Why extract features?
Motivation: panorama stitching
  We have two images – how do we combine them?
Step 1: extract features
Step 2: match features
Step 3: align images